## Slide 1: Fault prediction for bearings Anomaly detection with Deep Learning
Robert Anglberger
www.linkedin.com/in/robert-anglberger
https://github.com/devbert/Fault-prediction-for-bearings-anomaly-detection-
Author:
Linkedin:
Github:

## Slide 2: Fault prediction for bearings Anomaly detection with Deep Learning
Robert Anglberger
www.linkedin.com/in/robert-anglberger
https://github.com/devbert/Fault-prediction-for-bearings-anomaly-detection-
Author:
Linkedin:
Github:
3 days before crash!

## Slide 3: Agenda
Functional
Use Case
Data Set
Technical
Data Preparation
Data Exploration
Modeling
Model Performance
Solution
Data Products

## Slide 4: Functional
Use Case
Data Set
Solution
Data Products

## Slide 5: Use Case
Motor with 4 bearings installed on a shaft
Goal: predict when the bearings should be maintained or replaced
Functional

## Slide 6: Data Set
IoT sensor data from 4 bearings
Recording duration: Feb 12th 2004 – Feb 19th 2004
984 files / 20,840 records per file
File recording interval: Every 10 min
At the end of the test-to-failure experiment outer race failure occurred in bearing 1
Functional

## Slide 7: Solution
Deep Learning Neural Network and KNN
IBM Cloud with Watson Studio
Jupyter Python Notebook
Very low need of system resources (storage volume, CPU, RAM…)
Functional
3 days before crash!
Notes: I only had 1 vCPU and GB Ram available in my cloud environment so I took care about storage volume and system performance

## Slide 8
Coding - separated
bearing.etl.python.01.ipynb
bearing.model_def.python.07.ipynb
bearing.model_train.python.02.ipynb
bearing.model_evaluate.python.01.ipynb
Coding – all in one
bearing.model_deployment.python.03.ipynb
Presentation
Presentation file for Stakeholders and for technical audience
Functional
Data Products

## Slide 9: Technical
Data Preparation & Exploration
Modeling
Model Performance

## Slide 10
Technical
ETL
Data load from local file system
Data Transformation and loading to python dataframe

## Slide 11: ETL
Technical
Data Visualization
Data Sampling (10 min intervals)
Data Scaling

## Slide 12: Modeling
Unsupervised machine learning
  Autoencoder Neural Network with LSTM
  Autencoder Neural Network
  KNN Classification
Technical
Notes: We have to deal with unsupervised machine learning because we have no idea which parts of the measure points are normal and which are not. Which means we have no classification with good or bad

## Slide 13: Recurrent NN with LSTM
LSTM (long-short term memory)
Autoencoder
Technical
Notes: Autoencoder: The aim of an autoencoder is to learn a representation (encoding) for the bearing IoT data for dimensionality reduction by training the network to ignore signal “noise”. Along with the reduction side, a reconstructing side is learnt, where the autoencoder tries to generate from the reduced encoding a representation as close as possible to its original input

## Slide 14: Recurrent NN without LSTM
Only with Dense Layers
Autoencoder
Disadvantages compared to LSTM
  Gradient vanishing and exploding problems
  It cannot process very long sequences if using tanh or relu as an activation function.
Technical

## Slide 15: KNN Classification
Installed from package pyod
Anomaly detection in multivariate data
k Nearest Neighbors uses the distance to the kth nearest neighbor as the outlier score
Technical
Notes: Method: median, mean, largest which did not make a big difference in our bearing case

## Slide 16: Performance evaluation
Get loss of training data and identify threshold for anomaly
Plot the calculated loss distribution with threshold
Interpretation of result with domain expert
Technical
Notes: By plotting the distribution of the calculated loss in the training set I can use this to identify a suitable threshold value for identifying an anomaly. In doing this, I can make sure that this threshold is set above the “noise level”, and that any flagged anomalies should be statistically significant above the noise background

## Slide 17: Performance LSTM model
Technical

## Slide 18: Performance Recurr NN
Technical

## Slide 19: Performance KNN
Technical

## Slide 20: Result Summary
Similar result for both NN networks in this case
No good classification result for KNN
Technical

## Slide 21: Possible improvements
Technical
Model parameter optimization
Further code cleaning and optimization (e.g. use of object store instead of csv)
Use of Spark ML to improve scalability and performance
Use of SAP HANA database to improve performance
etc…..

## Slide 22
22
THANKS!
Any questions?
www.linkedin.com/in/robert-Anglberger
All coding and the presentation is available on GitHub:
https://github.com/devbert/Fault-prediction-for-bearings-anomaly-detection-